## Slide 1
Does Network Connectivity
Matter More Than Coverage?
Simulating Bike Lane Effects on Cycling Adoption

## Slide 2
Motivation & Research Question
Does bike lane connectivity have a greater effect on cycling mode share than total lane coverage?
If a much shorter connected lane structure results in as many commuters biking as a longer total milage lane set up, this is important to know from a policy/urban planning perspective.
Social observation among commuters amplifies infrastructure-induced mode shift.

## Slide 3
Model Environment
Downtown
Connected lanes
Residential
20×20 grid
each cell = one city block
200-300 agents
commuters with fixed home ↔ work
Zone split
downtown (central r=4) vs. residential
Work placement (Home placement is same fraction reversed)
90% downtown, 10% residential
Commute path
precomputed via Manhattan distance
Lane layer
Boolean property per cell; fixed at init

## Slide 4
Agent Decision Logic
1
Compute cost difference
Cost to bike and take a car depend on fixed cost values
Cost to bike incorporates a safety bonus from lanes multiplied by lane coverage
Difference of bike cost and car cost are computed
2
Observe neighbors
Von Neumann neighborhood (r = 1)
Compute social influence = fraction of neighbors biking
3
Update probability
probability_of_biking = logistic(cost_difference + social_influence)
4
Deterministic choice
'bike' if probability of biking > bike threshold, otherwise car
Threshold is a tunable parameter

## Slide 5
Scenarios & Batch Design
Scenario | Lane Coverage | Connectivity | Role
Baseline | None | None | Control
Low coverage, fragmented | Low | Low | Scattered lanes, minimal network
Low coverage, connected | Low | High | Core comparison: smaller but coherent
High coverage, fragmented | High | Low | Core comparison: larger but scattered
High coverage, connected | High | High | Upper bound — max infrastructure
Primary Core Test: low coverage connected vs. high coverage fragmented — does smaller connected network outperform larger fragmented network?
Secondary Core Test: high coverage connected vs. high coverage fragmented — does coverage still perform better than random placement?